## Slide 1
www.secnrs.ru
Approaches to Evaluation of Spent Nuclear
Fuel Reprocessing Products Activity and Volume
Equivalence which is Returned to a Supplier State in the Russian Federation
International Conference on the Management of Spent Fuel from Nuclear Power Reactors:
Learning from the Past, Enabling the Future
Vienna, 24 – 28 June, 2019
Federal Environmental, Industrial and Nuclear Supervision Service
(Rostechnadzor)
Scientific and Engineering Centre for
Nuclear and Radiation Safety
A. V. KURYNDIN, A. M. KIRKIN, S. V. MAKOVSKIY (SEC NRS), I. V. GUSAKOV-STANYUKOVICH, A. S. NOVIKOV, A. A. SHCHEKOCHIKHIN (JSC «TENEX»)

## Slide 2
www.secnrs.ru
States where Russian Power Units are Constructed ore Operated
The Russian Federation is a world leader in construction of power units abroad
Currently more than 30 power units with VVER-type reactors are being constructed in the world
During operation of foreign power units Russian specialists provide technical and scientific cooperation

## Slide 3
www.secnrs.ru
Handling with SNF of Power Units Located Outside the Russian Federation
Nuclear fuel for power units of foreign NPPs is supplied by the Russian Federation
Spent nuclear fuel (SNF) after several years of preliminary storage on NPP is sent to the Russian Federation for its technological storage and reprocessing
Fresh nuclear fuel
SNF
Russian Federation
Foreign NPP

## Slide 4
www.secnrs.ru
Return of SNF Reprocessing Products
SNF = U + Pu + М.А. (Np, Am, Cm, etc.) + FP (137Cs, 90Sr, 144Ce , etc.)
Spent nuclear fuel is characterized by high level of radioactivity and in order to sustain radioecological balance the activity equivalent of foreign SNF shall be returned to its supplier
Due to complexity of SNF composition evaluation of activity equivalent is a complicated process

## Slide 5
www.secnrs.ru
No 170-FZ «On the Use of Nuclear Energy»
Decree of the Government of the Russian Federation of 11.07.2003 No. 418
Safety guide
RB-092-13
Federal
laws
Methods for determination of the activity equivalent
(unique in every case)
No 7-FZ «On environmental protection»
Legal and Regulatory Basis for Return of SNF Reprocessing Products
Acting regulatory documents establish that activity equivalent of SNF imported to the Russian Federation shall be returned in a form of reprocessing products
Current practice implies the return of activity equivalent in the form of solidified high-level radioactive waste in accordance with recommendations of RB-092-13

## Slide 6
www.secnrs.ru
A criteria of dose equivalents (Sv) of SNF and reprocessing products (HLW) equality at the time of return is used
Dose equivalent is determined as a sum of dose equivalents of all radionuclides in SNF/HLW
The dose equivalents of nuclear materials in SNF are not taken into account in the calculations
Methodology of Evaluation of Activity Equivalence of SNF and Reprocessing Products in a Form of High-Level Waste (1/3)

## Slide 7
www.secnrs.ru
Methodology of Evaluation of Activity Equivalence of SNF and Reprocessing Products in a Form of High-Level Waste (2/3)
The dose equivalent of a single radionuclide is determined by dose coefficient and activity
Dose coefficients are established in Radiation Safety Standard (NRB-99/2009) (harmonized with ICRP publications)
NRB-99/2009
Chart: Dose coefficient, Sv/Bk
| Cs-137 | Sr-90 | Ru-106 | Cm-242
 | 1.3e-08 | 5e-08 | 4.9e-08 | 7.6e-08
Some examples of dose equivalents

## Slide 8
www.secnrs.ru
Methodology of Evaluation of Activity Equivalence of SNF and Reprocessing Products in a Form of High-Level Waste (3/3)
Approximate time scale of SNF handling
Chart: Periods after the reactor core discharge, years
| 1 | 3 | 5 | 7 | 10 | 20 | 30 | 50 | 80 | 100
 | 1156568619.3085 | 549386148.999 | 405852270.6628 | 359365380.649 | 327942780.658 | 268628610.011 | 225231429.2217 | 163249423.03 | 109428211.0801 | 88523491.9253
Storage in cooling pool
SNF technological storage and reprocessing in Russia
Return of the activity equivalent of reprocessing products
SNF import

## Slide 9
www.secnrs.ru
Approaches to Return of SNF Reprocessing Products (1/4)
Current approach
return to a supplier state of SNF dose equivalent in a form of HLW which are is vitrified in aluminophosphate matrix and contain full specter of radionuclides
Perspective approaches
№ 1
return to a supplier state of SNF dose equivalent in a form of HLW which are is vitrified in borosilicate matrix and contain only isotopes Cs+Sr and they decay products
№ 2
taking into account nuclear materials in SNF and return of dose equivalent in a form of fresh MOX or REMIX fuel and HLW with full specter of radionuclides
№ 3 (combined approach)
return to a supplier state of SNF dose equivalent in a form of MOX or REMIS fuel and HLW, containing only Cs+Sr fraction

## Slide 10
www.secnrs.ru
Approaches to Return of SNF Reprocessing Products (2/4)
Approach No 1 (Return of fractionated HLW)
HLW (Сs+Sr)
SNF
Advantages
Possible reduction of HLW volume (due to concentration of more activity in HLW)
No necessity to construct repositories for final disposal of HLW in deep geological formations
Disadvantages
Fractionation technology is now under development

## Slide 11
www.secnrs.ru
Approach No 2 (return of fuel with regenerated nuclear materials)
HLW + fuel (MOX, REMIX)
SNF
Advantages
Reduction of HLW volume due to use of regenerated materials in fuel cycle
Economy due to reduction of natural uranium consumption
Disadvantages
Need of additional justification of possibility of regenerated fuel loading in a core
Approaches to Return of SNF Reprocessing Products (3/4)

## Slide 12
www.secnrs.ru
Approach No 3 (combined)
HLW (Cs+Sr) + fuel (MOX, REMIX)
SNF
Advantages
Large reduction of HLW volume (up to full compensation by fuel)
Economy due to reduction of natural uranium consumption
No necessity to construct repositories for final disposal of HLW in deep geological formations
Disadvantages
Analogical to disadvantages of approaches No 1 and 2
Approaches to Return of SNF Reprocessing Products (4/4)

## Slide 13
www.secnrs.ru
Preliminary Analysis of HLW Mass which shall be Returned in Different Scenarios
Assumptions
Reactor type – VVER-1200
Initial enrichment of SNF– 4,95 % of 235U
Burnup– 60 GWt∙day/HMt
Time of storage in pool on NPP – 10 years
Return of reprocessing products is implemented after 20 years after discharge
Quantity of returned HLW significantly decreases if regenerated nuclear materials are involved and
HLW is fractionated
- 15 %
- 90 %
- 70 %
- 75 %
- 96 %
Chart: Mass of HLW/SFA, kg
| HLW only | HLW + REMIX | HLW + MOX
Not fractionated | 2128 | 1848 | 264
Cs+Sr only | 667 | 580 | 87

## Slide 14
www.secnrs.ru
Conclusion
Current Russian approach to return of SNF reprocessing products is approved by previous experience and implemented in methods of HLW return which are produced during reprocessing of VVER-type reactors and research reactors fuel
Current approach can be additionally improved through the involvement of the regenerated nuclear materials and fractionation of HLW
Volume of radioactive waste to be returned to the Supplier’s state significantly reduces (up to 96 %) in case of the return of the SNF activity equivalent in the form of fresh uranium-plutonium fuel (REMIX or MOX fuel) and HLW in borosilicate matrix, which contain only isotopes of Cs and Sr
The presented approaches could be used for development of new methodology of return of reprocessing products for SNF of foreign Russian-developed power units, which will be possible competitive advantage of Russian technologies on market

## Slide 15
Federal Environmental, Industrial and Nuclear Supervision Service
Scientific and Engineering Centre for Nuclear and Radiation Safety
Thank you for attention!
www.secnrs.ru